## Slide 1: Trichotillomania

## Slide 2: Excoriation

## Slide 3: Onychophagia

## Slide 4: Body-Focused Repetitive Behavior

## Slide 5: Development of Microcontroller Based Wearable Device with Monitoring System for Body-Focused Repetitive Behavior

## Slide 6: Rationale
Body-focused repetitive behavior (BFRB) is a term that refers to a group of compulsive habits that unintentionally harm one's body and alter one's appearance (Abrahams & Trotzky, 2017). In a related study published in npj Digital Medicine, a team lead by Child Mind Institute researchers found that utilizing heat sensors in addition to inertial measurement and proximity sensors, a wearable tracking system they designed achieves greater accuracy in position tracking.
This project will assist in the treatment of the Body-Focused Repetitive Behavior (BFRB patient). The device will be able to send a signal to the patient by using the vibration motor; it has a trained model implemented to the microcontroller by using its accelerometer and gyroscope in addition of distance sensor to improve the accuracy.

## Slide 7: Objectives of the Study
To develop a microcontroller based wearable technology that conveys a signal to the patient.
To embed mobile application for motion sensors in real time.
To assist in the treatment of the Body-Focused Repetitive Behavior (BFRB patient) with the proposed project.

## Slide 8: Our inspiration
The “Tingle” by npj Digital Medicine, Child Mind Institute - They disassembled and used N68 Fitness Tracker (ref) as their main component for their PCB along with the MCU and IMU. However besides of the appearance, the price is on the expensive side and is not affordable for the public use.
https://hackaday.io/project/144350-hacking-wearables-for-mental-health-and-more

## Slide 9: Our inspiration
doi.org/10.1038/s41746-019-0092-2

## Slide 10: Our inspiration
The “Keen” created by HabitAware – uses a gesture recognition for the initial use that makes the device recognize such habit. It then transmits a vibration signal to the patient wearing the device. Despite that, no published peer-reviewed study has shown the effectiveness of this device. There are testimonies that are presented in their website, but these are not great evidence to say that the device is well-suited for BFRB monitoring or treatment.
https://habitaware.com/

## Slide 11: Methodology MATERIALS
Arduino Nano 33 BLE Sense - Microcontroller
VL53L0X ToF Sensor – Proximity
Pulse Sensor – Tracker
Micro Vibration Motor – Haptic Feedback
Hand crafted Chassis – device’s chassis

## Slide 12: Arduino Nano 33 BLE Sense

## Slide 13: Accelerometer

## Slide 14: Gyroscope

## Slide 15: Micro Vibration Motor

## Slide 16: Distance sensor

## Slide 17: Pulse sensor

## Slide 18: 3.7V 110mAh Lithium Polymer Battery

## Slide 19: Charger Module
Step-up converter

## Slide 20: Methodology SOFTWARE
Python
  TensorFlow Lite – platform for machine learning
  Django – web framework (handles backend)
JavaScript
  Web BLE – connection for specific UUID (Universally Unique Identifier)
  CRC32 powered file transfer – cyclic redundancy check over the trained model file
  Plotting module – handles the real time graph
C++
  Arduino – MCU board

## Slide 23: Methodology TESTING
Unit & Integration test – each features completion
System test – complete product validation
User acceptance – patient evaluation with BFRB disorder

## Slide 24: Budgetary Estimate
Purpose | Component | Quantity | Unit Cost (Php)
Microcontroller | Arduino Nano 33 BLE Sense | 1 | 3,762
Proximity | VL53L0X ToF Sensor | 1 | 117
Tracker | Pulse Sensor | 1 | 136
Haptic Feedback | Micro Vibration Motor | 1 | 35
Power | 601220 Lithium Polymer Battery | 1 | 108
 | TP4056 Charger Module | 1 | 25
Connections | SPDT Slide Switch | 1 | 12
 | Stranded Wire | 2 | 10
 | Jumper Wire | 20 | 60
Chassis | Handcrafted wristwatch case | 1 | 200
Total |  |  | 4,465
Overall estimated cost = Php 5,100

## Slide 25: Expected Output

## Slide 26
~ Framing only

## Slide 30: In the future, we should get …
CRC32 – block size effectiveness
Neural Network – accuracy rate
BFRB – test on three said types
Sensors – dependencies to have an accurate prediction

## Slide 32: Gantt Chart of Activities

## Slide 33: Thank you!
Ryan Christopher D. Bahillo & Iriks Maria B. Dalanon
BS in Computer Engineering, 4-1